## Slide 1: Nextgen solutions
Building and implementing an airport network INFRASTRUCTURE

## Slide 2: Airport Requirements
Network
Connection
To PE airport
Internet Access
Networked PCs
For shops
Central Server
Cameras

## Slide 3: Proposed topology

## Slide 6: Gantt chart overview
Preparation : 2022/09/05 – 2022/09/09
  Includes drilling of holes, CCTV system setup, biometrics, fire suppression.
Server Room Setup : 2022/09/05 – 2022/09/09
  Floor lifting, drilling server mounts, mount racks, air conditioning , cleaning, installing Servers & firewall
Cable Room & Trunking : 2022/09/08 – 2022/09/26
  Cabling of all rooms in the building
Configuration of Network : 2022/09/22 – 2022/09/28
  MLS, Access Switches, Servers & Routers
Network Testing : 2022/09/29 – 2022/10/04
System Hand Over : 2022/09/05

## Slide 7: Ip ADDRESSING
DHCP
Used to assign IP addresses with VLAN tag to network devices.
STATIC IP
For security reasons, servers have been assigned static IP address

## Slide 8: Routing
            OSPF

## Slide 9: HSRP

## Slide 10: ZONE BASED FIREWALL
Configured with two zones, the Inside & Outside zones.
Inside to Outside Protocols:
  Icmp
  http
  https
  ftp
  Outside to Inside Protocols:
    Icmp
    ftp

## Slide 11: Nat translations & statistics

## Slide 12: Vpn tunnel
VPN Tunnel between the Main Router & PE Airport Router.
Phase 1
  Policy 110
  Encryption AES (128 bits)
  Authentication Pre-shared (NextGen)
  DH group 2
  Lifetime 3600
Phase 2
  transform-set MYSET esp-aes 128 esp-sha-hmac

## Slide 13: Thank You
QUESTIONS ?